## Slide 1: Rayvon
Real-time raycasting for VR in Mantle
Felipe Gomez-Frittelli
15-418 Final Project S'15

## Slide 2: Raycasting for Visibility
Interactive rendering applications determine visibility and coverage by rasterization
This has two requirements / drawbacks:
  Need(?) a uniform grid of coverage samples
  Have to sample entire image at once (or incur cost of repeatedly transforming objects)
Raycasting can solve these problems!
  Test visibility only where you want to, when you want to!

## Slide 3: Why raycasting?
Head-mounted displays (HMD) require very high resolution
  But maybe not uniform resolution
  Eye tracking in future displays will make foveal rendering a real possibility
To prevent "simulation sickness" very low latency is also required
  If the user moves his/her head, the camera must follow
  From Oculus SDK best practices:
    At least 75 fps
    <15 ms sensor-to-pixel latency (10 ms is ideal)

## Slide 4: Why raycasting?
Rasterization requires the entire frame to be rendered in advance
But displays don't read entire images at once ...
...they read one pixel at a time, in rows (or 'scanlines')!
Instead of preparing the entire image before the first row is scanned, why not just prepare the first row?
  Sample visibility by casting rays through pixels just ahead of the display scan-out
  "Beam-chasing" raycaster

## Slide 5: Rayvon Project Goals
HLSL raycasting functions mappable to any shader stage
  Rays are primitives in graphics - they should fit naturally into any renderer
Real-time raycasting and foveal rendering in Mantle
  Show that interactive raycasting is feasible for VR-quality scenes
  Not a recursive raytracer!
Synchronize raycasting with display read-out
  How close to the "beam" can we get?

## Slide 6: Why Mantle?
Mantle is a new, low-level graphics API from AMD
Designed to bring console-style memory and command buffer control to PC's, allowing deeper optimization at cost of programmer effort
Mantle also provides synchronization tools that avoid the CPU
  Detect scanline read position from display
  Signal 'events' in active command buffers - launch rays when they are needed, without waiting in a CPU thread

## Slide 7: HLSL raycasting
Mantle takes input from compiled shaders, typically written in HLSL
An HLSL implementation is portable and fits in any engine
Two options for implementing raycasting:
  HLSL Compute - GPGPU programming similar to CUDA
    No memory manipulation (HLSL shader resources, no pointers)
    No ballot() intrinsic!
  Graphics stages (VS, HS, DS, GS, PS)
    Shader model 5.0 allows any resources bound to any stage!

## Slide 8: Our approach: raycasting in shaders
A ray is just a point with metadata (direction, min/max t, etc.)
  a.k.a. a vertex!
We can take advantage of the GPU scheduler
  No atomic input/output buffers for rays
  Input rays are just a mesh - a list of vertices
  Output is to an image - no intermediate state necessary
  The GPU scheduler defaults to packet tracing - a batch of rays in a shader launch

## Slide 9: A Simple Pipeline
Each Vertex Shader launch is a packet trace!
Vertex Buffer
(Screen-space sample positions)
Vertex Shader:
Transform screen-to-world
Perform ray-bvh intersection
Compute shaded color
Pixel Shader:
Pass-through
(Can apply image ops, blending, etc.)
Render Target
Structured Buffers
Scene geometry
BVH
Material Data

## Slide 10: A complex, foveal pipeline
"Raycast" is an effect that can execute in any stage!
Structured Buffers
(Scene data)
Vertex Buffer
(Screen-space sample positions)
Vertex Shader:
Fetch indexed quads (screen tiles)
Hull Shader:
Compute tess factors by distance from focal point
Domain Shader:
Raycast and shade
Geom. Shader:
Form output quads
Pixel Shader:
Bilinearly interpolate ray samples over screen tiles
Render Target
TESS

## Slide 11: Rayvon Project Status
World's coolest ray-triangle intersection :D
Simplistic, barebones raycaster in Mantle
  Samples primary visibility per-pixel, outputs simple N-dot-L color to screen
Fast raycasting for real scenes requires good acceleration structures
  An original goal of this project was to implement fast BVH construction on GPU
  This turned out to take more time than I had available, and is hampered by lack of fast sort and ballot() intrinsic in HLSL

## Slide 12: Next Steps
Offline SBVH construction as a preprocess
BVH traversal in HLSL shaders
  No global ray pools, no re-shuffling of rays within warps
    Packets are independent and execute when/wherever the GPU scheduler can fit them
    No access to shared memory except in compute shaders
  While-while loop with leaves postponed in per-thread memory
    Best performance for primary rays - generally coherent packets
Sync draw calls per-row with scanline reads from an Oculus via LiquidVR